## Slide 1: Introduction to Integrated Assessment Modeling
Görkem Güngör
E-mail: ggungor@enerji.gov.tr

## Slide 2: Socio-economic Scenarios
Socio-economic scenarios are exclusively produced using Integrated Assessment Models (IAMs)
IAMs are large-scale, complex numerical models that represent interactions among environmental, technological and human systems
MESSAGE, IMAGE, MARIA, AIM, MiniCam and ASF were selected to develop SRES reference scenarios
IAMC created in 2007 together with a consortium agreement with the IPCC
Variety and convergence among IAMs
Notes: Cointe, B., Cassen, C., & Nadaï, A. (2019). Organising Policy-Relevant Knowledge for Climate Action. Science & Technology Studies, 32(4), 36–57. https://doi.org/10.23987/sts.65031

## Slide 3: Biogeochemical Cycle
Notes: IPCC, 2013: Climate Change 2013: The Physical Science Basis. Contribution of Working Group I to the Fifth Assessment Report of the Intergovernmental Panel on Climate Change [Stocker, T.F., D. Qin, G.-K. Plattner, M. Tignor, S.K. Allen, J. Boschung, A. Nauels, Y. Xia, V. Bex and P.M. Midgley (eds.)]. Cambridge University Press, Cambridge, United Kingdom and New York, NY, USA, 1535 pp.
Achard, F., Eva, H. D., Mayaux, P., Stibig, H.-J., & Belward, A. (2004). Improved estimates of net carbon emissions from land cover change in the tropics for the 1990s. Global Biogeochemical Cycles, 18(2). https://doi.org/10.1029/2003GB002142

## Slide 4: Earth System Interactions
Notes: http://serc.carleton.edu/introgeo/earthsystem/index.html

## Slide 5: Integrated Assessment Modeling
Policies are chosen to maximize the social welfare function with utility and labor inputs
Economic well being of future generations are discounted
Temperature increase is used as input for damages to production
Radiative forcing is used as input for temperature increase
Carbon emissions impose social cost to the economy
Notes: https://williamnordhaus.com/dicerice-models
Traeger, C. P. (2021). ACE – Analytic Climate Economy. SSRN Electronic Journal, October. https://doi.org/10.2139/ssrn.3832722
Kat, B., Paltsev, S., & Yuan, M. (2018). Turkish energy sector development and the Paris Agreement goals: A CGE model assessment. Energy Policy, 122(July), 84–96. https://doi.org/10.1016/j.enpol.2018.07.030

## Slide 6: Rebound Effect
Energy efficiency (EE) and electrification investments may increase the final electricity demand Price based instruments (taxes, caps) effect the welfare of consumers
Product specifications are considered as a bundle (performance vs. efficiency)
Social behaviour may prevent EE investments (public transport vs. private car)
Save energy vs. reduce carbon emission
Notes: Colmenares, G., Löschel, A., & Madlener, R. (2020). The rebound effect representation in climate and energy models. Environmental Research Letters, 15(12), 123010. https://doi.org/10.1088/1748-9326/abc214
Jarke-Neuert, J., & Perino, G. (2020). Energy efficiency promotion backfires under cap-and-trade. Resource and Energy Economics, 62, 101189. https://doi.org/10.1016/j.reseneeco.2020.101189

## Slide 7: Social and Environmental Development
Increasing energy security and job creation with clean energy
Procuring the least cost power generation
Diversifying the fuel mix to increase security of supply
Reducing fossil-fuel consumption
Improving energy access
Mitigating climate change and other environmental risks
Increasing private sector investment in the renewables sector
Notes: https://renewables-online.de/

## Slide 8: Baseline Energy System - Westeros
Notes: This example is based on the Westeros Tutorial - Introduction to the MESSAGEix framework: Creating a baseline scenario.

## Slide 9: Model Structure
The model horizon spans three decades (690-720)
Far in the future after the events of A Song of Ice and Fire (which occur ~300 years after Aegon the conqueror)
The discount ratio is 5% per year
Notes: https://awoiaf.westeros.org/index.php/Aegon%27s_Conquest

## Slide 10: Energy Demand
Demand for electricity is correlated with production
GDP profile is similar to first world historical profiles in the beginning of the 20th century
Model assumptions:
  40 million people in 300 AC
  Similar population growth to Earth in the same time frame (~factor of 12)
  A per capita demand for electricity of 1000 kWh

## Slide 11: Technology Parameters
Technology | Main input | Main output | Efficiency
Light bulb | Elec./Final | Light/Useful | 1
Grid | Elec./Secon. | Elec./Final | 0.9
Coal_ppl |  | Elec./Secon | 
Wind_ppl |  | Elec./Secon | 
Activity costs | USD / kWyr
Electricity grid | 50
Coal power plant | 30
Investment costs | USD / kW
Light bulb | 5
Coal power plant | 500
Wind power plant | 1500
Fixed costs | USD / kW/yr
Coal power plant | 30
Wind power plant | 10
Operating lifetime | Years
Light bulb | 10
Coal power plant | 20
Wind power plant | 20
Historical capacity addition | MW/year
Light bulb | 12224 (690-699)
Coal power plant | 2685 (680-699)
Wind power plant | 4755 (680-699)
Capacity factor | Share
Wind power plant | 0.36

## Slide 12: Historical Capacity
Electricity generation from coal and wind power plants
New capacity needs to be created to replace the retiring capacity and meet increasing demand
New capacity is created only when the investment cost is defined
Reference year capacity | MW
Light bulb | 55008
Coal_ppl | 38932.5
Wind_ppl | 68947.5

## Slide 13: Running the Problem
Select the «adb» scenario from «Select -> scenario
Generate the lineer programming matrix from «Run -> mxg»
Run the optimization solver from «Run -> opt»
Select the «Results -> interactive» screen to see the results in tables and graphs
Rows | 49 | Equations
Cols | 16 | Variables
Elms | 116 | Parameters
Rhs | 21 | Right hand side constraints
Bnds | 2 | Constant bounds

## Slide 14: Baseline Scenario
Secondary Electricity
Total installed capacity
Chart: Region: westeros_baseline, Scenario: adb Unit: MW
| 2700 | 2710
coal_ppl/total inst cap | 38932.5 | 83408
wind_ppl/total inst cap | 68947.5 | 21397.5
Chart: producers of fuel Electricity on level Secondary Region: westeros_baseline, Scenario: adb Unit: MWyr
| 2700 | 2710
coal_ppl/electricity | 36290 | 83408
wind_ppl/electricity | 24821.1 | 7703.1
Notes: Problem: westeros_baseline_adb
Rows: 49
Columns: 16
Non-zeros: 116
Status: OPTIMAL
Objective: func = 90595161.57 (MINimum)

## Slide 15: Introducing Emissions
Coal power plants emit CO2 causing air pollution and stimulating climate change
Copy "westeros_baseline" to "westeros_emission" to develop a new scenario
Define coal resources and primary energy sources as the model uses the technology input for emission calculation
Define CO2 emissions as a cumulative constraint
Include the CO2 emission factor to coal power plant technology
Emission factor | Factor
Coal power plant | 7.4 tCO2/kWyr
Emission bound | Cap
CO2 emissions | 8000 MtCO2 or 400 MtCO2/yr

## Slide 16: Emissions Cumulative Bound Scenario
Secondary Electricity
Total installed capacity
Chart: producers of fuel electricity on level secondary Region: westeros_emission, Scenario: adb Unit: MWyr
| 2700 | 2710
coal_ppl/electricity | 36290 | 63710
wind_ppl/electricity | 24821.1 | 27401.1
Chart: Region: westeros_emission, Scenario: adb Unit: MW
| 2700 | 2710
coal_ppl/total inst cap | 38932.5 | 63710
wind_ppl/total inst cap | 68947.5 | 76114.2
Notes: Problem: westeros_emission_adb
Rows: 55
Columns: 20
Non-zeros: 128
Status: OPTIMAL
Objective: func = 119,422,348.2 (MINimum)

## Slide 17: Emissions Cumulative Bound Scenario
Electricity price
Chart: shadow price of fuel electricity on level final Region: westeros_emission, Scenario: adb Unit: US$'00/kWyr
| 2700 | 2710
final/electricity | 290.86 | 505.69
CO2 emission
Chart: CO2 Emission Region: westeros_emission, Scenario: adb Unit: ktCO2/yr
| 2700 | 2710
CO2/value | 268546 | 471454

## Slide 18: Emissions Annual Bound Scenario
Secondary Electricity
Chart: producers of fuel electricity on level secondary Region: westeros_yearly, Scenario: adb Unit: MWyr
| 2700 | 2710
coal_ppl/electricity | 36290 | 54054.1
wind_ppl/electricity | 24821.1 | 37057.1
Total installed capacity
Chart: Region: westeros_yearly, Scenario: adb Unit: MW
| 2700 | 2710
coal_ppl/total inst cap | 38932.5 | 54054.1
wind_ppl/total inst cap | 68947.5 | 102936.3
Notes: Problem: westeros_yearly_adb
Rows: 56
Columns: 20
Non-zeros: 128
Status: OPTIMAL
Objective: func = 133,553,382.9 (MINimum)

## Slide 19: Emissions Annual Bound Scenario
Electricity price
Chart: shadow price of fuel electricity on level final Region: westeros_yearly, Scenario: adb Unit: US$'00/kWyr
| 2700 | 2710
final/electricity | 83.33 | 505.69
CO2 emission
Chart: CO2 Emission Region: westeros_yearly, Scenario: adb Unit: ktCO2/yr
| 2700 | 2710
CO2/value | 268546 | 400000.34

## Slide 20: External Costs
Coal power plant utilities can benefit from generating additional electricity
The benefit from creating additional electricity from coal power plants causes additional CO2 emission
Annual constraint creates a shadow price defined as the benefit gained from additional electricity generation per additional CO2 emission
The price is what the coal power plant utilities are willing to pay – therefore negative
Chart: Region: westeros_yearly, Scenario: adb Unit: US$'00/tCO2
| 2700 | 2710
CO2/shadow price | 0 | -41.11

## Slide 21: Emissions Tax Scenario
Secondary Electricity
Chart: producers of fuel electricity on level secondary Region: westeros_tax, Scenario: adb Unit: MWyr
| 2700 | 2710
coal_ppl/electricity | 36290 | 63710
wind_ppl/electricity | 24821.1 | 27401.1
Total installed capacity
Chart: Region: westeros_tax, Scenario: adb Unit: MWyr
| 2700 | 2710
coal_ppl/electricity | 36290 | 63710
wind_ppl/electricity | 24821.1 | 27401.1
Notes: Problem: westeros_tax_adb
Rows: 56
Columns: 20
Non-zeros: 129
Status: OPTIMAL
Objective: func = 212,650,767.7 (MINimum)

## Slide 22: Emissions Tax Scenario
Electricity price
Chart: shadow price of fuel electricity on level final Region: westeros_tax, Scenario: adb Unit: US$'00/kWyr
| 2700 | 2710
final/electricity | 83.35 | 505.69
CO2 emission
Chart: Region: westeros_tax, Scenario: adb Unit: ktCO2/yr
| 2700 | 2710
CO2/value | 268546 | 471454

## Slide 23: Discussion
Emission bound generates a shadow price for additional CO2 emission which can be traded between utilities
The revenues collected by emission tax can be used for subsidizing clean energy generation through feed-in-tariffs
The achievement of the climate target requires using a basket of policy instruments from energy supply and demand sectors
Notes: Description
This image includes recognisable people, being impacted locally. Research suggests making this link as tangibly as possible is crucial for engaging audiences and situating climate change in the ‘here and now’.
© Ashley Cooper / Aurora Photos

## Slide 24: Recommendations
Learn GAMS together with student license from https://www.ifpri.org/publication/agrodep-gams-training-toolbox
Follow the announcements and the recent developments from https://www.iamconsortium.org/newsletter-subscription/
Try to master at least one programming language
Reach out to others and share your ideas – remember that climate action requires collaborative effort
Notes: Description
Research has found that telling ‘local’ visual stories is an important component for effective engagement – showing real people, in a range of regional contexts, being affected by and responding to climate change.
© Peter Essick / Aurora
https://www.yesmagazine.org/opinion/2020/10/23/climate-literacy-effective-change

## Slide 25: References
[1] Cointe B, Cassen C, Nadaï A. Organising Policy-Relevant Knowledge for Climate Action. Sci Technol Stud [Internet]. 2019. 32(4):36–57.
[2] Traeger CP. ACE – Analytic Climate Economy. SSRN Electron J [Internet]. 2021. (October).
[3] Kat B, Paltsev S, Yuan M. Turkish energy sector development and the Paris Agreement goals: A CGE model assessment. Energy Policy [Internet]. 2018. 122(July):84–96.
[4] Colmenares G, Löschel A, Madlener R. The rebound effect representation in climate and energy models. Environ Res Lett [Internet]. 2020. 15(12):123010.
[5] Jarke-Neuert J, Perino G. Energy efficiency promotion backfires under cap-and-trade. Resour Energy Econ [Internet]. 2020. 62:101189.